## Slide 1: Robot_Hand Project
Wiring Diagram and Code
Author: Peter Chan
Date: 12 Sept 2017

## Slide 2: Arduino Nano board pinout

## Slide 3: Project Robot_Hand - transmitter
HC-05 module
(Master)
EN: No Connection
VCC: 5V
GND: 0V
TXD: D10
RXD D11 (3.3V)
STATE: No Connection
Power Switch
2KΩ
3.7V x 2 18650 Battery
Demo
Switch
10kΩ
Flex Sensor 1
(potentiometer)
10kΩ
Flex Sensor 2
(potentiometer)
10kΩ
Flex Sensor 3
(potentiometer)
10kΩ
Flex Sensor 4
(potentiometer)
10kΩ
Flex Sensor 5
(potentiometer)
RXD
VCC
1KΩ

## Slide 4: Project Robot_Hand - receiver
HC-05 module
(Master)
EN: No Connection
VCC: 5V
GND: 0V
TXD: D10
RXD D11 (3.3V)
STATE: No Connection
Power Switch
2KΩ
3.7V x 2 18650 Battery
Test
Switch
RXD
VCC
1KΩ
3.7V x 2 18650 Battery
5V
7.2V
5V
7.2V
Power
Switch

## Slide 5
Contact: Peter W. Chan
Email: peter_w_chan@outlook.com

## Slide 6: HC-05 and HC-06 Bluetooth transceiver and receiver
Bluetooth is a wireless technology standard for exchanging data over short distances (using short-wavelength UHF radio waves in the ISM band from 2.4 to 2.485 GHz) from fixed and mobile devices, and building personal area networks (PANs). Range is approximately 10 Meters (30 feet).
HC-05 is a more capable module that can be set to be either Master or Slave for Bluetooth communication. Transmission distance is 20m~30m in free space
HC-06 is a Slave only device for Bluetooth communication. HC-05 or Android/iPhone/PC device are required for initiate the Bluetooth communication.
These small HC-05/HC-06 modules run on 3.3V power with 3.3V signal levels.
The module has two modes of operation, Command Mode where we can send AT commands to it and Data Mode where it transmits and receives data to another Bluetooth module.
Further Information:
https://arduino-info.wikispaces.com/BlueTooth-HC05-HC06-Modules-How-To
http://www.instructables.com/id/How-to-Configure-HC-05-Bluetooth-Module-As-Master-/

## Slide 7: HC-05 / HC-06 Bluetooth and Arduino
Since HC-05/HC-06 RX pin accept 3.3 volts only, you need to have a voltage divider (e.g. 1kΩ and 2kΩ resistor in series) to spit Arduino output pin’s voltage from 5 volts into 1.67 volts and 3.33 volts for RX pin.
Note: TX pin could stay as 3.3 volts as Arduino could recognise a HIGH from 3 volts to 5 volts.
HC-06 default settings: Slave only | Baud Rate: 9600,n,8,1 | Pin Code: 1234
HC-05 default settings: Slave (Master/Slave) | Baud Rate: 38400,n,8,1 | Pin Code: 1234 | Connection mode: Bluetooth device specified
HC-05/HC-06 LED light status:
  Wait for Bluetooth connection: Blinking continuously every 1 second
  Enter AT command mode: Blinking continuously every 2-3 seconds
  Bluetooth communication established: Flashing every few seconds interval

## Slide 8: HC-05 module setup for BT communication
Steps to enter AT command mode for HC-05 Bluetooth module:
Connect the HC-05 module as following:
  Vcc (HC-05)  5V (Arduino)
  Gnd (HC-05)  GND (Arduino)
  TXD (HC-05)  D10 (Arduino pin 10)
  RXD (HC-05)  D11 (Arduino pin 11)
  KEY (HC-05)  D9 (Arduino pin 9)
  Note: Avoid Tx1 and Rx0 pin at Arduino so that serial communication between PC and Arduino will not be affected.
Before connecting the Arduino board to the USB cable, REMOVE THE VCC WIRE FROM THE HC-05. Only after you have removed the VCC wire, connect the USB to the Arduino board.
Download the sample source code (file name: AT mode) and upload it into your Arduino board.
After the uploading process is complete, press the button in HC-05 module before reconnecting the VCC wire back to your HC-05 module
LED on the HC-05 Bluetooth module should blink for every 2 seconds interval. This indicates that the Bluetooth module has entered AT mode.
Open the Serial Monitor and ensure you have change "No Line Ending" to "Both NL & CR" and fix the baud rate at 9600 at the bottom right hand corner of the window. For about 1 second, a sentence saying "Enter AT commands:" will pop up.
To see whether everything is okay or not, enter "AT" and send. An "OK" will pop up on the Serial Monitor and this implies that no problems occur.
Note: KEY (HC-05) pin could be left open or ground for normal BT communication (i.e. Data Mode). Use “SoftwareSerial” built-in Arduino library to configure the HC-05/HC-06 Bluetooth module
https://www.arduino.cc/en/Reference/SoftwareSerial

## Slide 9: Configure HC-05 using module AT commands
Slave Configuration:
The required AT commands to set the configuration
  AT+RMAAD (To clear any paired devices)
  AT+ROLE=0 (To set it as slave)
  AT+ADDR (To get the address of this HC-05, remember to jot the address down as it will be used during master configuration)
  AT+UART=38400,0,0 (To fix the baud rate at 38400)
If the commands entered are replied with "OK" then it indicates that the settings mentioned have been customized.
You may also try out other AT commands such as how to change the name, the password, and so on.
Note that the password for both master and slave must be the same otherwise pairing will not be done.
Master Configuration:
The required AT commands to set the configuration:
  AT+RMAAD (To clear any paired devices)
  AT+ROLE=1 (To set it as master)
  AT+CMODE=0 (To connect the module to the specified Bluetooth address and this Bluetooth address can be specified by the binding command)
  AT+BIND=xxxx,xx,xxxxxx (Now, type AT+BIND=98d3,34,906554 obviously with your respective address to the slave. Note the commas instead of colons given by the slave module.
  AT+UART=38400,0,0 (To fix the baud rate at 38400)
If the commands entered are replied with "OK" then it indicates that the settings mentioned have been customized.
You may also try out other AT commands such as how to change the name, the password, and so on.
Note that the password for both master and slave must be the same otherwise pairing will not be done.